## Slide 2: Spanning-Tree Protocol

## Slide 3: A switched network with switching loops

## Slide 4: A switched network with STP

## Slide 5: Spanning-tree Terms
Root bridge: The root bridge is the bridge with the lowest and, therefore, the best bridge ID.
Bridge ID: It's determined by a combination of the bridge priority, which is 32,768 by default on all Cisco switches, and the base MAC address. The bridge with the lowest bridge ID becomes the root bridge in the network.
BPDU: All switches exchange information to use for the subsequent configuration of the network. Each switch compares the parameters in the Bridge Protocol Data Unit (BPDU) . Inside the BPDU is the bridge ID.

## Slide 6: Bridge Port Roles
Root port: The root port is the link with the lowest path cost to the root bridge.
Designated port: A designated port is one that's been determined to have the best (lowest) cost to get to on a given network segment, compared to other ports on that segment.
Forwarding port: A forwarding port forwards frames and will be either a root port or a designated port.
Blocked port: A blocked port won't forward frames in order to prevent loops.

## Slide 7: In-class Practice

## Slide 8: Convergence
Convergence occurs when all ports on bridges and switches have transitioned to either forwarding or blocking modes.
No data will be forwarded until convergence is complete. Yes—you read that right: When STP is converging, all host data stops transmitting through the switches!

## Slide 9: Link Cost
Port cost is the cost of a single link whereas path cost is the sum of the various port costs to the root bridge.

## Slide 10: STP operations

## Slide 11: STP operations

## Slide 12: STP operations

## Slide 13: Bridge ID

## Slide 14: Types of Spanning-tree Protocols
IEEE 802.1d: The original standard for bridging and STP, which is really slow but requires very little bridge resources. It's also referred to as Common Spanning Tree (CST). PVST+: The Cisco proprietary enhancement for STP that provides a separate 802.1d spanning-tree instance for each VLAN. Know that this is just as slow as the CST protocol, but with it, we get to have multiple root bridges.
IEEE 802.1w: Also called Rapid Spanning Tree Protocol (RSTP), this iteration enhanced the BPDU exchange and paved the way for much faster network convergence, but it still only allows for one root bridge per network like CST. Rapid PVST+: Cisco's version of RSTP that also uses PVST+ and provides a separate instance of 802.1w per VLAN. It gives us really fast convergence times and optimal traffic flow but predictably requires the most CPU and memory of all.

## Slide 15: Common STP example

## Slide 16: PVST+ provides efficient root bridge selection.

## Slide 17: PVST+ unique bridge ID

## Slide 18: RSTP example 1

## Slide 19: RSTP example 1 answer

## Slide 20: RSTP example 2

## Slide 21: RSTP example 2, answer 1

## Slide 22: RSTP example 2, answer 2

## Slide 23: How are the designated ports chosen?
To choose the switch that will forward on the segment, we select the switch with the lowest accumulated path cost to the root bridge. We want the fast path to the root bridge.
If there is a tie on the accumulated path cost from both switches to the root bridge, then we'll use bridge ID
Port priorities can be set manually if we want a specific port chosen. The default priority is 32, but we can lower that if needed.
If there are two links between switches, and the bridge ID and priority are tied, the port with the lowest number will be chosen—for example, Fa0/1 would be chosen over Fa0/2.

## Slide 24: Modifying and Verifying the Bridge ID

## Slide 25: Our simple three-switch network

## Slide 26: S3’s output

## Slide 27: Set the priority
You can set the priority to any value from 0 through 61440 in increments of 4096.
Setting it to zero (0) means that the switch will always be a root as long as it has a lower MAC address than another switch that also has its bridge ID set to 0.

## Slide 28: Enable RSTP on a Cisco switch

## Slide 29: STP stopping loops

## Slide 30: STP failure

## Slide 31: PortFast

## Slide 32: Before and after port channels

## Slide 33: Written Labs and Review Questions