## Slide 1
CCNA Routing and Switching Study Guide
Chapters 3 & 17: Enhanced IGRP
Instructor & Todd Lammle

## Slide 2: Chapter 17 objectives
The ICND2 topics covered in this chapter include:
IP Routing Technologies
  Differentiate methods of routing and routing protocols
  Administrative distance
  split horizon
  metric
  next hop
  Configure and verify EIGRP (single AS)
  Feasible Distance / Feasible Successors / Administrative distance
  Feasibility condition
  Metric composition
2

## Slide 3: Chapter 17 objectives (con’t)
The ICND2 topics covered in this chapter include:
IP Routing Technologies
  Router ID
  Auto summary
  Path selection
  Load balancing
  Equal
  Unequal
  Passive interface
  Troubleshooting
  Troubleshoot and resolve routing issues
  Routing is enabled
  Routing table is correct
  Correct path selection
  Troubleshoot and resolve EIGRP problems
  Neighbor adjacencies
  AS number
  Load balancing
  Split horizon
3

## Slide 4: EIGRP
Enhanced Interior Gateway Routing Protocol (EIGRP) is a Cisco protocol that runs on Cisco routers and on some Cisco switches.
EIGRP has a number of features that make it especially useful within large, complex networks. A real standout among these is its support of VLSM, which is crucial to its ultra-efficient scalability. EIGRP even includes benefits gained through other common protocols like OSPF and RIPv2, such as the ability to create route summaries at any location we choose.
EIGRP is a classless, distance-vector protocol that uses the concept of an autonomous system to describe a set of contiguous routers that run the same routing protocol and share routing information, which also includes the subnet mask in its route updates.

## Slide 5: EIGRP Features and Operations
EIGRP is a classless, distance-vector protocol that uses the concept of an autonomous system to describe a set of contiguous routers that run the same routing protocol and share routing information, which also includes the subnet mask in its route updates.
EIGRP is sometimes referred to as a hybrid routing protocol or an advanced distance-vector protocol
  EIGRP has link-state characteristics as well—it synchronizes network topology information between neighbors at startup and then sends specific updates only when topology changes occur (bounded updates).

## Slide 6: EIGRP neighbor discovery
And these three things will be exchanged with directly connected neighbors:
Hello or ACK received
AS numbers match
Identical metrics (K values)
Before EIGRP routers can exchange routes with each other, they must become neighbors, and there are three conditions that must be met before this can happen.

## Slide 7: Advertised distance
Reported/advertised distance (AD)
This is the metric of a remote network, as reported by a neighbor. It’s also the routing table metric of the neighbor and is the same as the second number in parentheses as displayed in the topology table. The first number is the administrative distance. In the figure, routers SF and NY are both advertising the path to network 10.0.0.0 to the Corp router, but the cost through SF to network 10.0.0.0 is less than NY.

## Slide 8: Feasible distance
Feasible distance (FD)
This is the best metric among all paths to a remote network, including the metric to the neighbor that’s advertising the remote network. The route with the lowest FD is the route that you’ll find in the routing table because it’s considered the best path. The metric of a feasible distance is calculated using the metric reported by the neighbor that’s referred to as the reported or advertised distance plus the metric to the neighbor reporting the route.
In the figure, the Corp router will have the path through router SF to network 10.0.0.0 in the routing table since it’s the lowest feasible distance. It’s the lowest true cost from end to end.

## Slide 9: The tables used by EIGRP

## Slide 10: Five different types of packets used by EIGRP
Update: An Update packet contains route information. When these are sent in response to metric or topology changes, they use reliable multicasts. In the event that only one router needs an update, it's sent via unicasts.
Query: A Query packet is a request for specific routes and always uses the reliable multicast method.
Reply: A Reply packet is sent in response to a query via the unicast method. Replies either include a specific route to the queried destination or declare that there's no known route. Hello: A Hello packet is used to discover EIGRP neighbors and is sent via unreliable multicast, meaning it doesn't require an acknowledgment. ACK: An ACK packet is sent in response to an update and is always unicast.

## Slide 11: Diffusing Update Algorithm (DUAL)
I mentioned that EIGRP uses Diffusing Update Algorithm (DUAL) for selecting and maintaining the best path to each remote network. DUAL allows EIGRP to carry out these vital tasks:
Figure out a backup route if there's one available.
Support variable length subnet masks (VLSMs).
Perform dynamic route recoveries.
Query neighbors for unknown alternate routes.
Send out queries for an alternate route.

## Slide 12: Configuring our little internetwork with EIGRP
Corp#config t
Corp(config)#router eigrp 20
Corp(config-router)#network 172.16.0.0
Corp(config-router)#network 10.0.0.0

## Slide 13: VSLM Support and Summarization
Corp#config t
Corp(config)#router eigrp 20
Corp(config-router)#network 10.10.11.0 0.0.0.255
Corp(config-router)#network 172.16.10.0 0.0.0.3
Corp(config-router)#network 172.16.10.4 0.0.0.3

## Slide 14: Discontiguous networks
Always typing in no auto-summary under RIPv2 and EIGRP is common practice today.
To solve discontiguous networks, always typing in no auto-summary under RIPv2 and EIGRP is common practice today.

## Slide 15: Route selection with EIGRP
EIGRP uses a combination of these four factors to compare routes and select the best possible path:
Bandwidth
Delay
Load
Reliability

## Slide 16: EIGRP route selection process

## Slide 17: Routing table on the Corp router
172.16.0.0/30 is subnetted, 2 subnets
C 172.16.10.4 is directly connected, Serial0/1
C 172.16.10.0 is directly connected, Serial0/0
10.0.0.0/24 is subnetted, 6 subnets
C 10.10.10.0 is directly connected, GigabitEthernet0/0
C 10.10.11.0 is directly connected, GigabitEthernet0/1
D 10.10.20.0 [90/3200000] via 172.16.10.2, 00:00:27, Serial0/0
D 10.10.30.0 [90/3200000] via 172.16.10.2, 00:00:27, Serial0/0
D 10.10.40.0 [90/2297856] via 172.16.10.6, 00:00:29, Serial0/1
D 10.10.50.0 [90/2297856] via 172.16.10.6, 00:00:30, Serial0/1

## Slide 18: After adding the network 192.168.10.0/24
Corp#sh ip eigrp topology
IP-EIGRP Topology Table for AS(20)/ID(10.10.11.1)
Codes: P - Passive, A - Active, U - Update, Q - Query, R - Reply,
r - reply Status, s - sia Status
P 10.10.10.0/24, 1 successors, FD is 128256
via Connected, GigbitEthernet0/0
P 10.10.11.0/24, 1 successors, FD is 128256
via Connected, GigbitEthernet0/1
P 10.10.20.0/24, 1 successors, FD is 2300416
via 172.16.10.6 (2300416/156160), Serial0/1
via 172.16.10.2 (3200000/128256), Serial0/0
P 10.10.30.0/24, 1 successors, FD is 2300416
via 172.16.10.6 (2300416/156160), Serial0/1
via 172.16.10.2 (3200000/128256), Serial0/0
P 10.10.40.0/24, 1 successors, FD is 2297856
via 172.16.10.6 (2297856/128256), Serial0/1
via 172.16.10.2 (3202560/156160), Serial0/0
P 10.10.50.0/24, 1 successors, FD is 2297856
via 172.16.10.6 (2297856/128256), Serial0/1
via 172.16.10.2 (3202560/156160), Serial0/0
P 192.168.10.0/24, 1 successors, FD is 2172416
via 172.16.10.6 (2172416/28160), Serial0/1
via 172.16.10.2 (3074560/28160), Serial0/0
P 172.16.10.4/30, 1 successors, FD is 2169856
via Connected, Serial0/1
P 172.16.10.0/30, 1 successors, FD is 3072000
via Connected, Serial0/0

## Slide 19: Split horizon in action, part 1

## Slide 20: Split horizon in action, part 2

## Slide 21: EIGRP troubleshooting commands
Command | Description/Function
show ip eigrp neighbors | Shows all EIGRP neighbors
show ip eigrp interfaces | Lists the interfaces on which the router has actually enabled EIGRP
show ip route eigrp | Shows EIGRP entries in the routing table
show ip eigrp topology | Shows entries in the EIGRP topology table
show ip eigrp traffic | Shows the packet count for EIGRP packets sent and received
show ip protocols | Shows information about the active protocol sessions

## Slide 22: Troubleshooting scenario
Here are some key things to look for if neighbors haven’t formed an adjacency:
Interfaces between the devices are down.
The two routers have mismatching EIGRP autonomous system numbers.
Proper interfaces are not enabled for the EIGRP process.
An interface is configured as passive.
The K values are mismatched.
EIGRP authentication is misconfigured.
Also, if the adjacency is up, but you’re not receiving remote network updates, there may be a routing problem, likely caused by these issues:
The proper networks aren’t being advertised under the EIGRP process.
An access list is blocking the advertisements from remote networks.
Automatic summary is causing confusion in your discontiguous network.

## Slide 23: Configuring EIGRPv6 on our Internetwork
Corp#config t
Corp(config)#ipv6 router eigrp 10
Corp(config-rtr)#no shut
Corp(config-rtr)#router-id 1.1.1.1
Corp(config-rtr)#int s0/0/0
Corp(config-if)#ipv6 eigrp 10
Corp(config-if)#int s0/0/1
Corp(config-if)#ipv6 eigrp 10
Corp(config-if)#int g0/0
Corp(config-if)#ipv6 eigrp 10
Corp(config-if)#int g0/1
Corp(config-if)#ipv6 eigrp 10

## Slide 24: Written Labs and Review Questions
  Read through the Exam Essentials section together in class.
  Open your books and go through all the written labs and the review questions.
  Review the answers in class.
24