## Slide 1
CCNA Routing and Switching Study Guide
Chapters 7 & 21: Wide Area Networks
Instructor & Todd Lammle

## Slide 2: WAN terms
Customer premises equipment (CPE) is equipment that’s typically owned by the subscriber and located on the subscriber’s premises.

## Slide 3: WAN terms
Demarcation (demarc for short) is the precise spot where the service provider’s responsibility ends and the CPE begins.

## Slide 4: WAN terms
Local loop connects the demarc to the closest switching office, referred to as the central office.

## Slide 5: WAN terms
Central office (CO) connects the customer’s network to the provider’s switching network, also referred to as a point of presence (POP)

## Slide 6: WAN terms
Toll network is a trunk line inside a WAN provider’s network. This network is a collection of switches and facilities owned by the Internet service provider (ISP).

## Slide 7: WAN connection types

## Slide 8: Broadband access using cable or DSL

## Slide 9: Cable network and terms

## Slide 10: xDSL connection from home user to central office. All types of DSL are layer 1 technologies.
The term xDSL covers a number of DSL variations, such as Asymmetrical DSL (ADSL), high-bit-rate DSL (HDSL), Rate Adaptive DSL (RADSL), Synchronous DSL (SDSL), ISDN DSL (IDSL), and very-high-data-rate DSL (VDSL)

## Slide 11: PPPoE with ADSL
Asymmetrical DSL (ADSL) supports both voice and data at the same time, but it was created to allot more bandwidth downstream than upstream
Used with ADSL services, PPPoE (Point-to-Point Protocol over Ethernet) encapsulates PPP frames in Ethernet frames and uses common PPP features like authentication, encryption, and compression.

## Slide 12: DTE-DCE-DTE WAN
The idea behind a WAN is to be able to connect two DTE networks through a DCE network. The DCE network includes the CSU/DSU, through the provider’s wiring and switches, all the way to the CSU/DSU at the other end.
DTE-DCE-DTE WAN connection: Clocking is typically provided by the DCE network to routers. In nonproduction environments, a DCE network is not always present.

## Slide 13: High-Level Data-Link Control (HDLC) Protocol
A popular ISO-standard, bit-oriented, Data Link layer protocol.
HDLC is the default encapsulation used by Cisco routers over synchronous serial links.

## Slide 14: Configuring Cisco’s HDLC proprietary WAN encapsulation
Corp(config)#int s0/0
Corp(config-if)#ip address 172.16.10.1 255.255.255.252
Corp(config-if)#no shut
Corp#sh int s0/0
Serial0/0 is up, line protocol is up
Hardware is PowerQUICC Serial
Internet address is 172.16.10.1/30
MTU 1500 bytes, BW 1544 Kbit, DLY 20000 usec,
reliability 255/255, txload 1/255, rxload 1/255
Encapsulation HDLC, loopback not set
Keepalive set (10 sec)

## Slide 15: Point-to-Point Protocol (PPP)
A Data Link layer protocol that can be used over either asynchronous serial (dial-up) or synchronous serial (ISDN) media.
PPP is to transport layer 3 packets across a Data Link layer point-to-point link
Unless you have all Cisco routers, you need PPP on your serial interfaces because the HDLC encapsulation is Cisco proprietary

## Slide 16: PPP protocol stack compared to the OSI reference model.

## Slide 17: PPP session establishment

## Slide 18: Configuring PPP Authentication
Router(config)#int s0
Router(config-if)#encapsulation ppp
Router#config t
Router(config)#hostname RouterA
RouterA(config)#username RouterB password cisco
RouterA(config)#int s0
RouterA(config-if)#ppp authentication chap pap

## Slide 19: Failed PPP authentication

## Slide 20: Mismatched WAN encapsulations

## Slide 21: Mismatched IP addresses
Pod1R1#sh int s0/0
Serial0/0 is up, line protocol is up
Hardware is PowerQUICC Serial
Internet address is 10.0.1.1/24
MTU 1500 bytes, BW 1544 Kbit, DLY 20000 usec,
reliability 255/255, txload 1/255, rxload 1/255
Encapsulation PPP, loopback not set
Keepalive set (10 sec)
LCP Open
Open: IPCP, CDPCP

## Slide 22: Single-Homed EBGP
Border Gateway Protocol (BGP) is perhaps one of the most well-known routing protocols in the world of networking
BGP powers the Internet and makes possible connecting to remote systems on the other side of the country or planet.
If you’re configuring BGP between a customer network and an ISP, this process is called external BGP (EBGP)

## Slide 23: Configuring and Verifying EBGP
Basic information to configure EBGP
  AS numbers (your own, and all remote AS numbers)
  All the neighbors (peers) that are involved in BGP, and IP addressing that is used among the BGP neighbors
  Networks that need to be advertised into BGP

## Slide 24: EBGP network layout
AS=1
AS=100
AS=200
192.168.1.1
192.168.2.1
192.168.2.2
192.168.1.2
Lo0: 10.0.0.0
Lo0: 10.0.1.0
Lo0: 10.0.2.0
ISP
R1
R2

## Slide 25: Three main steps to configure BGP
Define the BGP Process
example: router bgp 1
Establish one or more neighbor relationships
example: neighbor 192.168.1.2 remote-as 100
neighbor 192.168.2.2 remote-as 200
Advertise the local networks into BGP
example: network 10.0.0.0 mask 255.255.255.0

## Slide 26: Verifying EBGP
Show ip bgp summary gives you an overview of the BGP status
Show ip bgp displays the entire BGP table
Show ip bgp neighbors provides more information about BGP connections to neighbors.

## Slide 27: Written Labs and Review Questions
  Read through the Exam Essentials section together in class.
  Open your books and go through all the written labs and the review questions.
  Review the answers in class.
27