## Slide 1
Sybex CCENT 100-101
Chapter 6: Cisco’s Internetworking Operating System (IOS)
Instructor & Todd Lammle

## Slide 2: Chapter 6 Objectives
The CCENT Topics Covered in this chapter include:
LAN Switching Technologies
  Configure and verify initial switch configuration including remote access management.
    Cisco IOS commands to perform basic switch setup
IP Routing Technologies
  Configure and verify utilizing the CLI to set basic Router configuration
    Cisco IOS commands to perform basic router setup
  Configure and verify operation status of an ethernet interface
    Verify router configuration and network connectivity
  Cisco IOS commands to review basic router information and network connectivity
Network Device Security
  Configure and verify network device security features such as
    Device password security
    Enable secret vs enable
    Transport
    Disable telnet
    SSH
    VTYs
    Physical security
    Service password
    Describe external authentication methods
Troubleshooting
  Troubleshoot and Resolve Layer 1 problems
    Framing
    CRC
    Runts
    Giants
    Dropped packets
    Late collision
    Input / Output errors
2

## Slide 3: Connecting to Cisco Devices
Console port
Telnet or SSH

## Slide 4: Bringing Up a Switch
When you first bring up a Cisco IOS device, it will run a power-on self-test—a POST. Upon passing that, the machine will look for and then load the Cisco IOS from flash memory if an IOS file is present, then expand it into RAM.
As you probably know, flash memory is electronically erasable programmable read-only memory—an EEPROM. The next step is for the IOS to locate and load a valid configuration known as the startup-config that will be stored in nonvolatile RAM (NVRAM).
Once the IOS is loaded and up and running, the startup-config will be copied from NVRAM into RAM and from then on referred to as the running-config.
But if a valid IOS isn’t found in NVRAM, your switch will enter setup mode, giving you a step-by-step dialog to help configure some basic parameters on it.

## Slide 5: Command-Line Interface (CLI)
After the interface status messages appear and you press Enter, the Switch> prompt will pop up. This is called user exec mode, or user mode for short, and although it’s mostly used to view statistics, it is also a stepping stone along the way to logging in to privileged exec mode, called privileged mode for short.
You can view and change the configuration of a Cisco router only while in privileged mode, and you enter it via the enable command like this:
Switch>enable
Switch#
Practice: enable, disable, logout

## Slide 6: Global Configuration Mode
Type config from the privileged-mode prompt and then press Enter to opt for the default of terminal like this:
Switch#config
Switch(config)#
At this point, you make changes that affect the router as a whole (globally), hence the term global configuration mode.

## Slide 7: CLI Prompts
interface
  To make changes to an interface
line
  To configure user-mode passwords
ip accecss-list standard
  To configure a standard named access list
Routing Protocol Configurations

## Slide 8: Interface
Switch(config)#interface ?
…………
Here ? Shows the possible commands related to interface
Switch(config)#interface fastEthernet 0/1
Switch(config-if)#
This shows you are in interface configuration mode

## Slide 9: Line Commands
Line commands:
Switch(config)#line?
Switch(config)#line console 0
Switch(config-line)#

## Slide 10: Access List Configurations
Switch(config)#ip access-list standard Todd
Switch(config-std-nacl)#

## Slide 11: Routing Protocol Configurations
Switch(config)#router rip
IP routing not enabled
Switch(config)#ip routing
Switch(config)#router rip
Switch(config-router)#

## Slide 12: Defining Router Terms
Mode | Definition
User exec mode | Limited to basic monitoring commands
Privileged exec mode | Provides access to all other router commands
Global configuration mode | Commands that affect the entire system [AU: Includes commands that affect…? Also in the next one? Doesn’t seem like the mode is commands.]leavee
Specific configuration modes | Commands that affect interfaces/processes only
Setup mode | Interactive configuration dialog
Table 6.1 defines some of the terms I’ve used so far.
Table 6.1: Router terms

## Slide 13: Table 6.2: Enhanced editing commands
Command | Meaning
Ctrl+A | Moves your cursor to the beginning of the line
Ctrl+E | Moves your cursor to the end of the line
Esc+B | Moves back one word
Ctrl+B | Moves back one character
Ctrl+F | Moves forward one character
Esc+F | Moves forward one word
Ctrl+D | Deletes a single character
Backspace | Deletes a single character
Ctrl+R | Redisplays a line
Ctrl+U | Erases a line
Ctrl+W | Erases a word
Ctrl+Z | Ends configuration mode and returns to EXEC
Tab | Finishes typing a command for you
Table 6.2: Enhanced editing commands
Table 6.2 lists the enhanced editing commands available on a Cisco router.

## Slide 14: Table 6.3: Router-command history
Command | Meaning
Ctrl+P or up arrow | Shows last command entered
Ctrl+N or down arrow | Shows previous commands entered
show history | Shows last 20 commands entered by default
show terminal | Shows terminal configurations and history buffer size
terminal history size | Changes buffer size (max 256)
Table 6.3: Router-command history
You can review the router-command history with the commands shown in Table 6.3.

## Slide 15: Help Command
“?” is very useful
Returns possible prompts
Example: set up the time on the switch
  Switch#clock ?
  Switch#clock set ?
  Switch#clock set 9:00:00 1 July 2015

## Slide 16: Read Feedback
After typing the command, reading the feedback is also important
  % Imcomplete command
  % Invalid input detected at ‘^’ marker
  % Ambiguous command: ..
Use ? to adjust your command

## Slide 17: Administrative Functions
You can configure the following administrative functions on a router and switch:
Hostnames
Banners
Passwords
Interface descriptions

## Slide 18: Hostnames/Banner
We use the hostname command to set the identity of the router. This is only locally significant, meaning it doesn’t affect how the router performs name lookups or how the device actually works on the internetwork.
  Switch#config t
  Switch(config)#hostname Todd
Message of the day (MOTD) banners are the most widely used banners because they give a message to anyone connecting to the router via Telnet or an auxiliary port or even through a console port as seen here:
  Todd(config)#banner motd ?
  LINE c banner-text c, where ‘c’ is a delimiting character
  Todd(config)#banner motd #
  Enter TEXT message. End with the character ‘#’.
  $ Acme.com network, then you must disconnect immediately.
  #
  Todd(config)#^Z (Press the control key + z keys to return to privileged mode)

## Slide 19: Passwords
Enable password/enable secret
  Todd(config)#enable secret todd
  - This is recommended
  Todd(config)#enable password todd
  The enable password you have chosen is the same as your enable secret. This is not recommended. Re-enter the enable password.
You wont use the older enable password in today’s networks.

## Slide 20: Console/VTY passwords
User-mode passwords are assigned via the line command like this:
  Todd(config)#line ?
  <0-16> First Line number
  console Primary terminal line
  vty Virtual terminal

## Slide 21: SSH
1. Set your hostname:
Router(config)#hostname Todd
2. Set the domain name—both the hostname and domain name are required for the encryption keys to be generated:
Todd(config)#ip domain-name Lammle.com
3. Set the username to allow SSH client access:
Todd(config)#username Todd password Lammle
    4. Generate the encryption keys for securing the session:
Todd(config)#crypto key generate rsa
5. Enable SSH version 2 on the router—not mandatory, but strongly suggested:
Todd(config)#ip ssh version 2
6. Connect to the VTY lines of the switch:
Todd(config)#line vty 0 15
7. Configure your access protocols:
Todd(config-line)#transport input ?
all All protocols
none No protocols
ssh TCP/IP SSH protocol
telnet TCP/IP Telnet protocol
Todd(config-line)#transport input ssh ?
telnet TCP/IP Telnet protocol
<cr>
But if you want to go with Telnet, here’s how you do that:
Todd(config-line)#transport input ssh telnet

## Slide 22: Encrypting Your Passwords
To manually encrypt your passwords, use the service password-encryption command. Here’s how:
Todd#config t
Todd(config)#service password-encryption
Todd(config)#exit
Todd#show run
Building configuration...
!
!
enable secret 4 ykw.3/tgsOuy9.6qmgG/EeYOYgBvfX4v.S8UNA9Rddg
enable password 7 1506040800

## Slide 23: Descriptions
Setting descriptions on an interface is another administratively helpful thing, and like the hostname, it’s also only locally significant.
Todd#config t
Todd(config)#int fa0/1
Todd(config-if)#description Sales VLAN Trunk Link
Todd(config-if)#^Z
Todd#
And on a router serial WAN:
Router#config t
Router(config)#int s0/0/0
Router(config-if)#description WAN to Miami
Router(config-if)#^Z

## Slide 24: Verifying interfaces
Todd#sh ip interface brief
Interface IP-Address OK? Method Status Protocol
Vlan1 192.168.255.8 YES DHCP up up
FastEthernet0/1 unassigned YES unset up up
FastEthernet0/2 unassigned YES unset up up
FastEthernet0/3 unassigned YES unset down down
FastEthernet0/4 unassigned YES unset down down
FastEthernet0/5 unassigned YES unset up up
FastEthernet0/6 unassigned YES unset up up
FastEthernet0/7 unassigned YES unset down down
FastEthernet0/8 unassigned YES unset down down
GigabitEthernet0/1 unassigned YES unset down down

## Slide 25: Gigabit Ethernet Example
Todd#config t
Todd(config)# interface GigabitEthernet 0/1
Todd(config-if)#speed 1000
Todd(config-if)#duplex full
Or just int g0/1
Slot/port

## Slide 26: Serial Interface Example
Todd(config)#interface serial ?
Todd(config)#interface serial 0/0/?
Todd(config)#interface serial 0/0/0
Slot/subslot/port
The first 0 is the router itself, then the slot and then the port.

## Slide 27: Bringing Up an Interface
If an interface is shut down, it’ll display as administratively down when you use the show interfaces command (sh int for short):
Router#sh int f0/0
FastEthernet0/1 is administratively down, line protocol is down
[output cut]
You can bring up the router interface with the no shutdown command (no shut for short):
Router(config)#int f0/0
Router(config-if)#no shutdown
*August 21 13:45:08.455: %LINK-3-UPDOWN: Interface FastEthernet0/0,
changed state to up
Router(config-if)#do show int f0/0
FastEthernet0/0 is up, line protocol is up
[output cut]

## Slide 28: Configuring IP address of an Interface
Todd(config)#int f0/1
Todd(config-if)#ip address 172.16.10.2 255.255.255.0

## Slide 29: Figure 6.4: Providing clocking on a nonproduction network

## Slide 30: Viewing, Saving, and Erasing Configurations
You can manually save the file from DRAM, which is usually just called RAM, to NVRAM by using the copy running-config startup-config command. You can use the shortcut copy run start as well:
  Todd#copy running-config startup-config
  Destination filename [startup-config]? [press enter]
  Building configuration...
  [OK]
  Todd#
  Building configuration...
When you see a question with an answer in [], it means that if you just press Enter, you’re choosing the default answer.

## Slide 31: Show running-config
You can view the files by typing show running-config or show startup-config from privileged mode. The sh run command, which is a shortcut for show running-config, tells us that we’re viewing the current configuration:
  Todd#sh run
  Building configuration...
  Current configuration : 855 bytes
  !
  ! Last configuration change at 23:20:06 UTC Mon Mar 1 1993
  !
  version 15.0
  [output cut]
NOTE: You can see the version of IOS with the show running-config command

## Slide 32: Show startup-config
The sh start command—one of the shortcuts for the show startup-config command—shows us the configuration that will be used the next time the router is reloaded. It also tells us how much NVRAM is being used to store the startup-config file.
  Todd#sh start
  Using 855 out of 524288 bytes
  !
  ! Last configuration change at 23:20:06 UTC Mon Mar 1 1993
  !
  version 15.0
  [output cut]
But beware—if you try and view the configuration and see
  Todd#sh start
  startup-config is not present
you have not saved your running-config to NVRAM, or you’ve deleted the backup configuration! Let me talk about just how you would do that now.

## Slide 33: Deleting the Configuration and Reloading the Device
You can delete the startup-config file by using the erase startup-config command:
Todd#erase startup-config
Todd#reload
NOTE: you can no longer use the shortcut commands for erasing the backupconfiguration.

## Slide 34: Other Commands
Sh int ?
Sh int f0/0
Sh int s0/0/0
Clear counters s0/0/0
Sh protocols
Sh ip interface
Sh ip int brief
Sh controllers serial 0/0

## Slide 35: Written Labs and Review Questions
  Read through the Exam Essentials section together in class
  Open your books and go through all the written labs and the review questions.
  Review the answers in class.
35