## Slide 1
Sybex CCENT 100-101
Chapter 7: Managing a Cisco Internetwork
Instructor & Todd Lammle

## Slide 2: Chapter 7 Objectives
The CCENT Topics Covered in this chapter include:
LAN Switching Technologies
  Verify network status and switch operation using basic utilities such as ping, telnet and ssh
IP Routing Technologies
  Configure and verify utilizing the CLI to set basic Router configuration
    Cisco IOS commands to perform basic router setup
  Verify router configuration and network connectivity
    Cisco IOS commands to review basic router information and network connectivity
IP Services
  Configure and verify DHCP (IOS Router)
    configuring router interfaces to use DHCP
    DHCP options
    excluded addresses
    lease time
  Configure and verify NTP as a client
2

## Slide 3: Table 7.1: Cisco router components
Bootstrap | Stored in the microcode of the ROM, the bootstrap is used to bring a router up during initialization. It boots the router up and then loads the IOS.
POST (power-on self-test) | Also stored in the microcode of the ROM, the POST is used to check the basic functionality of the router hardware and determines which interfaces are present.
ROM monitor | Again, stored in the microcode of the ROM, the ROM monitor is used for manufacturing, testing, and troubleshooting.
Mini-IOS | Called the RXBOOT or bootloader by Cisco, the mini-IOS is a small IOS in ROM that can be used to bring up an interface and load a Cisco IOS into flash memory. The mini-IOS can also perform a few other maintenance operations.
RAM (random access memory) | Used to hold packet buffers, ARP cache, routing tables, and also the software and data structures that allow the router to function. Running-config is stored in RAM, and most routers expand the IOS from flash into RAM upon boot.
ROM (read-only memory) | Used to start and maintain the router. Holds the POST and the bootstrap program as well as the mini-IOS.
Flash memory | Stores the Cisco IOS by default. Flash memory is not erased when the router is reloaded. It is EEPROM (electronically erasable programmable read-only memory) created by Intel.
NVRAM (nonvolatile RAM) | Used to hold the router and switch configuration. NVRAM is not erased when the router or switch is reloaded. Does not store an IOS. The configuration register is stored in NVRAM.
Configuration register | Used to control how the router boots up. This value can be found as the last line of the show version command output and by default is set to 0x2102, which tells the router to load the IOS from flash memory as well as to load the configuration from NVRAM.

## Slide 4: Router and Switch Boot Sequence
performs a POST
locates and loads the Cisco IOS software
looks for startup-config
copy startup-config and name it running-config

## Slide 5: Copying the Current Configuration to NVRAM
By copying running-config to NVRAM as a backup, as shown in the following output, you ensure that your running-config will always be reloaded if the router gets rebooted. Starting in the 12.0 IOS, you’ll be prompted for the filename you want to use:
  Router#copy running-config startup-config
  Destination filename [startup-config]?[enter]
  Building configuration...
  [OK]

## Slide 6: Verifying the Current Configuration
To verify the configuration in DRAM, use the show running-config command (sh run for short) like this:
  Router#show running-config
  Building configuration...
  Current configuration : 855 bytes
  !
  version 15.0
The current configuration information indicates that the router is running version 15.0 of the IOS.

## Slide 7: Copying the Configuration to a TFTP Server
Once the file is copied to NVRAM, you can make a second backup to a TFTP server by using the copy running-config tftp command, or copy run tftp for short. I’m going to set the hostname to Todd before I run this command:
  Todd#copy running-config tftp
  Address or name of remote host []? 10.10.10.254
  Destination filename [todd-confg]?
  !!
  776 bytes copied in 0.800 secs (970 bytes/sec)
If you have a hostname already configured, the command will automatically use the hostname plus the extension -confg as the name of the file.

## Slide 8: Restoring the Cisco Configuration
If you did copy the configuration to a TFTP server as a second backup, you can restore the configuration using the copy tftp running-config command (copy tftp run for short), or the copy tftp startup-config command (copy tftp start for short), as shown in the output below. Just so you know, the old command we used to use for this is config net:
  Todd#copy tftp running-config
  Address or name of remote host []?10.10.10.254
  Source filename []?todd-confg
  Destination filename[running-config]?[enter]
  Accessing tftp://10.10.10.254/todd-confg...
  Loading todd-confg from 10.10.10.254 (via FastEthernet0/0):
  !!
  [OK - 776 bytes]
  776 bytes copied in 9.212 secs (84 bytes/sec)
  Todd#
  *Mar 7 17:53:34.071: %SYS-5-CONFIG_I: Configured from
  tftp://10.10.10.254/todd-confg by console
Okay, here we can see that the configuration file is an ASCII text file, meaning that before you copy the configuration stored on a TFTP server back to a router, you can make changes to the file with any text editor.

## Slide 9: Erasing the Configuration
To delete the startup-config file on a Cisco router or switch, use the command erase startup-config, like this:
  Todd#erase startup-config
  Erasing the nvram filesystem will remove all configuration files!
  Continue? [confirm][enter]
  [OK]
  Erase of nvram: complete
  *Mar 7 17:56:20.407: %SYS-7-NV_BLOCK_INIT: Initialized the geometry of nvram
  Todd#reload
  System configuration has been modified. Save? [yes/no]:n
  Proceed with reload? [confirm][enter]
  *Mar 7 17:56:31.059: %SYS-5-RELOAD: Reload requested by console.
  Reload Reason: Reload Command.
This command deletes the contents of NVRAM on the switch and router. If you type reload while in privileged mode and say no to saving changes, the switch or router will reload and come up into setup mode.

## Slide 10: Configuring DHCP
Here are your configuration steps:
Exclude the addresses you want to reserve. The reason you do this step first is because as soon as you set a network ID, the DHCP service will start responding to client requests.
Create your pool for each LAN using a unique name.
Choose the network ID and subnet mask for the DHCP pool that the server will use to provide addresses to hosts.
Add the address used for the default gateway of the subnet.
Provide the DNS server address(es).
6. If you don’t want to use the default lease time of 24 hours, you need to set the lease time in days, hours, and minutes.

## Slide 11: Figure 7.1: DHCP Configuration example on a switch
Here’s how we’ll configure DHCP using the 192.168.10.0/24 network ID:
  Switch(config)#ip dhcp excluded-address 192.168.10.1 192.168.10.10
  Switch(config)#ip dhcp pool Sales_Wireless
  Switch(dhcp-config)#network 192.168.10.0 255.255.255.0
  Switch(dhcp-config)#default-router 192.168.10.1
  Switch(dhcp-config)#dns-server 4.4.4.4
  Switch(dhcp-config)#lease 3 12 15
First, you can see that I reserved 10 addresses in the range for the router, servers, and printers, etc. I then created the pool named Sales_Wireless, added the default gateway and DNS server, and set the lease to 3 days, 12 hours, and 15 minutes (which isn’t really significant because I just set it that way for demonstration purposes).

## Slide 12: DHCP Relay
But what happens if we need to provide an IP address from a DHCP server to a host that’s not in our broadcast domain, or if we want to receive a DHCP address for a client from a remote server?
So we know that because the hosts off the router don’t have access to a DHCP server, the router will simply drop their client request broadcast messages by default. To solve this problem, we can configure the F0/0 interface of the router to accept the DHCP client requests and forward them to the DHCP server like this:
  Router#config t
  Router(config)#interface fa0/0
  Router(config-if)#ip helper-address 10.10.10.254

## Slide 13: Verify DHCP on Cisco IOS
show ip dhcp binding Lists state information about each IP address currently leased to a client.
show ip dhcp pool [poolname] Lists the configured range of IP addresses, plus statistics for the number of currently leased addresses and the high watermark for leases from each pool.
show ip dhcp server statistics Lists DHCP server statistics—a lot of them!
show ip dhcp conflict If someone statically configures an IP address on a LAN and the DHCP server hands out that same address, you’ll end up with a duplicate address. We can use this command to check such conflict.

## Slide 14: Network Time Protocol (NTP)
NTP synchronizes clocks of computer systems over packetswitched, variable-latency data networks to keep all routers, switches, servers, etc. receiving the same time information.

## Slide 15: Figure 7.3: Sending console messages to a syslog server
A syslog server saves copies of console messages and can time-stamp them so you can view them at a later time. This is actually rather easy to do. Here would be your configuration on the SF router:
  SF(config)#logging host 172.16.10.1
  SF(config)#service timestamps log datetime msec

## Slide 16: Network Time Protocol (NTP)
To make sure all devices are synchronized with the same time information, we’ll configure our devices to receive the accurate time information from a centralized server
SF(config)#ntp server 172.16.10.1 version 4
SF(config)# sh ntp ?
SF(config)# sh ntp status
SF(config)# sh ntp associations

## Slide 17: Cisco Discovery Protocol (CDP)
A protocol designed by Cisco to help administrator to collect information about locally attached devices
#sh cdp
Show the parameters about CDP

## Slide 18: CDP Paramters
CDP timer: how often CDP packets are sent out;
CDP holdtime: how long the device will hold packets received from neighboring devices
#cdp holdtime ?
#cdp timer ?
#cdp run
#no cdp run

## Slide 19: Gathering Neighbor Information
#sh running-config
  Show IP and local interface info
#sh cdp neighbors
  Show neighbor device info
Administrators can use CDP to document network topology

## Slide 20: Using DNS to Resolve Names
So if you have a DNS server on your network, you’ll need to add a few commands to make DNS name resolution work well for you:
The first command is ip domain-lookup, which is turned on by default. It needs to be entered only if you previously turned it off with the no ip domain-lookup command.
The second command is ip name-server. This sets the IP address of the DNS server. You can enter the IP addresses of up to six servers.
The last command is ip domain-name. Although this command is optional, you really set it because it appends the domain name to the hostname you type in.
Here’s an example of using these three commands:
SW-1#config t
SW-1(config)#ip domain-lookup
SW-1(config)#ip name-server 4.4.4.4
SW-1(config)#ip domain-name lammle.com

## Slide 21: Debug
#ping
  test IP connectivity and name resolution using the DNS server
#traceroute
  shows path a packet takes to get to a remote device
#debug
  display information about various router operations and the related traffic, plus any error messages
#sh processes
  determine a given router’s CPU utilization
  provide a list of active processes

## Slide 22: Written Labs and Review Questions
  Read through the Exam Essentials section together in class
  Open your books and go through all the written labs and the review questions.
  Review the answers in class.
22